## Slide 1
Physics-Informed Adaptive Reward Generation for Sim-to-Real Dexterous Hand Control
Eureka • Adaptive Domain Randomization • PINN Failure Diagnosis • PPO on NVIDIA Isaac Lab
Final Year Project | Review 1 | Team: [Name / Roll], [Name], [Name] | Guide: [Name] | 2026

## Slide 2
Abstract & Problem Definition
2
• Reward engineering is the bottleneck in RL for dexterous manipulation.
- Eureka (ICLR'24) automates it: an LLM writes reward code from environment source, refined by evolutionary search + per-component reward reflection.
- DrEureka (RSS'24) adds LLM-generated domain randomization for zero-shot sim-to-real.
• Gap 1 - Reflection reports WHAT, never WHY.
- An inverted-sign reward bug and a contact-model mismatch produce near-identical feedback. The LLM has one tool - rewrite the reward - which is wrong for the second case, and the harm stays invisible until deployment.
• Gap 2 - Static DR is calibrated against a policy that no longer exists.
- DrEureka fixes ranges from an initial policy; range feasibility is a property of the CURRENT policy.
• Gap 3 - No channel through which 'the simulator is wrong' can be expressed.
PLATFORMS (both, cross-morphology)
----------------------------------
Sim : NVIDIA Isaac Lab 2.3.0
(Isaac Sim 5.1.0, Python 3.11)
RL : PPO via rl_games
- matches Eureka/DrEureka
for ablation validity
Task A: Isaac-Repose-Cube-Shadow
Shadow Hand, 24 joints / 20 act.
Task B: Isaac-Reorient-Cube-Leap
LEAP Hand, 16 DoF, + real robot
LLM : Gemini 3.5 Flash

## Slide 3
Objectives & Expected Outcomes
3
• O1 - Reproduce the Eureka/DrEureka baseline unmodified (rung 1).
- Inherited deliberately: reward loop, reflection, fitness metric, PPO. Unmodified inheritance is what makes the ablation interpretable.
• O2 - Adaptive domain randomization (Contribution 1).
- Re-evaluate DR ranges every N iterations from policy performance, closing DrEureka's one-shot loop.
• O3 - PINN physics-residual failure diagnosis + routing (Contribution 2).
- Separate 'fix the reward' from 'fix the physics assumptions'; enforce the separation in code.
• O4 - Ground-truth validation of the diagnosis (Contribution 3).
- Injection calibration + placebo arms. No prior work validates an attribution signal this way.
Outcome | How it is judged
Rung-1 fidelity | Matches published Eureka behaviour
Adaptive DR gain | Transfer vs static DR, held-out config
Diagnosis validity | AUC vs injected ground truth
Signal is load-bearing | Real vs shuffled vs no signal
Real transfer (LEAP) | Zero-shot on physical hand

## Slide 4
Scope & Feasibility
4
Component | IN scope | OUT of scope
Simulator | Isaac Lab 2.3.0 / Isaac Sim 5.1.0 | Isaac Gym (deprecated, archived Apr 2026)
Robots | Shadow Hand (sim), LEAP Hand (sim+real) | Arms, quadrupeds, locomotion
Observations | Proprioceptive state | Vision (no RT cores on datacenter GPUs)
RL algorithm | PPO (rl_games) | SAC/HER - would break baseline parity
PINN role | Failure diagnosis via physics residual | Contact-solver modification
LLM | Gemini 3.5 Flash (API) | Fine-tuning
COMPUTE - MEASURED, NOT ESTIMATED
---------------------------------
GPU : 1x NVIDIA L4, 23 GB
Driver : 595.71.05
Throughput : 1.70 s / epoch @ 8192 envs
(~77k FPS steady state)
Startup : ~53 s per process launch
Concurrency: 2 workers MAX
(3 exhausts system RAM)
Budget : ~376 GPU-hours for the
full 2-platform ladder
• All upstream code open-source; Phase 0 already installed, patched and validated end-to-end (see Progress slide).

## Slide 5
System Architecture - Two Loops, One Router
5
Task spec + safety instruction + environment source code
LLM (Gemini): generate K candidate reward functions
Parallel PPO training - Isaac Lab (Shadow Hand / LEAP Hand)
PINN physics residual (contact-phase gated)
Reward reflection + task fitness F
DIAGNOSIS ROUTER - classify: reward-logic error vs physics mismatch
reward-logic -> edit reward code
physics -> update DR ranges
Enforced in code, not requested in a prompt: each diagnosis can trigger only its own pathway.

## Slide 6
Algorithm 1 - Eureka Reward Synthesis (inherited unmodified)
6
Input: task description T, env source E, LLM M, iterations G, population K
1: R_0 <- M.generate(T, E, K) # K reward programs, zero-shot
2: for g in 0..G-1:
3: for r in R_g:
4: pi_r <- PPO_train(E, r) # Isaac Lab, parallel envs
5: s(r) <- F(pi_r) # task fitness - NEVER the LLM reward
6: ref(r)<- per_component_stats(r) # reward reflection
7: R_{g+1} <- M.mutate(T, best(R_g), ref)
8: return argmax_r s(r)
KEY DESIGN POINT (Eureka's actual insight):
reward MUST return a dict of NAMED components, not a scalar
-> turns an opaque score into a diagnosable signal
• Inherited without modification:
• Evolutionary search structure
• Reward reflection channel
• Task fitness F, unchanged from benchmark
• PPO + hyperparameters
• Why not modify it?
• Every change to the baseline weakens the ablation. Rung 1 must be a faithful reproduction or nothing above it is interpretable.

## Slide 7
Algorithm 2 - Adaptive Domain Randomization (Contribution 1)
7
DrEureka (baseline) | OURS (adaptive)
-----------------------------|---------------------------------
RAPP sweep on pi_initial | RAPP sweep -> initial ranges phi_0
LLM picks ranges within it | LLM picks ranges within it
ranges FIXED for training | every N iterations:
| perf <- fitness + reflection
| if robust : widen phi
| if failing: narrow phi
| (LLM-selected, within feasibility)
Why it matters: range feasibility is a property of the CURRENT
policy. A late robust policy tolerates far wider randomization
than the initial one RAPP was calibrated against.
• Implementation basis:
• LEAP_Hand_Isaac_Lab already ships a working ADR module (LeapHandADR) that widens EventTerm ranges on a fixed schedule.
• That is the mechanism. Our contribution is LLM-driven range SELECTION at each decision point - closing the loop ADR leaves open and DrEureka leaves one-shot.
• Honest caveat:
• DrEureka tested intra-training adaptation and found it unnecessary for locomotion. We hypothesise it matters where feasible ranges are narrow and contact dominates - and must demonstrate it, not assume it.

## Slide 8
PINN - Physics-Residual Failure Diagnosis (Contribution 2)
8
Equations of motion (Lagrangian form):
R_phys = M(q)*q_ddot + C(q,q_dot)*q_dot + G(q) + F_contact - tau
For ideal rigid-body dynamics, R_phys = 0. The residual therefore
measures how far observed SIMULATED behaviour departs from
consistent physics - i.e. how much is simulator artifact.
Loss (SOPDNA composite shape):
L_total = lam_d * L_data + lam_p * L_phys + lam_c * L_ctrl
lam_* have NO literature default - both source papers leave
them untuned. Ours are explicit tunable config, not constants.
• Why learned, not an analytic check:
• Evaluable at arbitrary / counterfactual states
• Continuous differentiable signal -> can be gated
• Latent parameter discovery: identifies WHICH physical parameter is mismatched -> exactly what the DR controller needs
• THE HARD PART - contact:
• Prior work (PI-DDPG, SOPDNA) handles only smooth dynamics. In-hand manipulation is discontinuous multi-point contact.
• Mitigation: contact-phase gating; contact-free and contact-phase residuals reported SEPARATELY, never aggregated.

## Slide 9
The Routing Rule - Why Separation Is Necessary
9
FAILURE MODE: reward shunting
• Give the LLM a physics signal with no constraint, and it does the natural thing: fixes the symptom in reward space - a penalty steering the policy away from the badly-modelled region.
• Result:
• Fitness improves. Ablation reports 'PINN helped'.
• But the physics error was never addressed - it was ABSORBED into the reward.
• That reward encodes avoidance of a simulator artifact the real robot does not have.
• So the naive integration looks like success, hides the cause, and DAMAGES the sim-to-real transfer the project exists to improve.
THE RULE: diagnose, then route
Diagnosis | Permitted | Forbidden
reward-logic error | Edit reward code | Touching DR ranges
physics mismatch | Update DR ranges | Editing reward code
• Three things at once:
• Makes the PINN's contribution MEASURABLE - otherwise 'physics helped' cannot be separated from 'extra text helped'.
• Prevents the transfer-harming failure above.
• Forces the signal to be load-bearing - a physics diagnosis is the ONLY thing that can move DR ranges.
• A dual diagnosis is rejected by design, keeping the routing audit interpretable as a confusion matrix.

## Slide 10
Validating the Diagnosis (Contribution 3)
10
• The claim 'high residual => physics failure' is an INFERENCE, not a fact.
• A bad reward can drive the policy into contact-rich, poorly-modelled states, producing a high residual from a pure reward bug. Without a test, the router routes on a confounded signal.
• 1. Injection calibration - a hard gate before any rung-3 claim
• Seed KNOWN reward bugs (sign flip, wrong scale, missing term) vs KNOWN dynamics shifts (mass x1.5, friction x0.3, added damping); measure discrimination AUC.
• Taxonomy drawn from failures ACTUALLY OBSERVED in rung 1 - not invented, or it measures detection of bugs no real LLM produces.
• 2. Placebo arms
• Real signal vs SHUFFLED signal vs no signal, identical budgets. If real ~= shuffled, the contribution is unsupported however good the AUC.
• 3. Routing audit
• Diagnosis -> edit-type logged every iteration; confusion matrix for the whole loop against injected ground truth.
AUC outcome | Decision
contact-free strong, contact-phase weak | EXPECTED. Proceed with contact-gated routing.
contact-free ALSO weak | STOP. Do not build the full router. Fall back, recalibrate, or report a negative result.
• Encoded as executable logic, not a judgement call made under deadline pressure.

## Slide 11
Data & Benchmarks
11
• There is NO fixed offline dataset. All training data is generated ONLINE by GPU-parallel simulation.
• This is inherent to the method: Eureka-style reward search requires fresh rollouts under each candidate reward, so a pre-collected corpus cannot serve it.
Corpus | Source | Role
Benchmark environments | Isaac Lab: Isaac-Repose-Cube-Shadow-Direct-v0; LEAP_Hand_Isaac_Lab: Isaac-Reorient-Cube-Leap | The two evaluation platforms
Rollout telemetry | Generated per step: joint pos/vel/torque, tracking error, contact events, active DR values | Reward reflection + summarizer
PINN corpus | Privileged sim transitions: hand state + object 6-DoF pose/twist + DR params | Self-supervised - physics residual IS the label
Injection corpus | Runs with deliberately seeded reward bugs vs seeded dynamics shifts | GROUND TRUTH for the AUC gate
Real-world eval | Physical LEAP Hand rollouts, zero-shot | Sim-to-real evidence
• Lineage note: the Shadow Hand task descends from Eureka's Bi-DexHands suite; the LEAP task from DrEureka. Object sets such as YCB are relevant only if the work is later extended beyond single-object cube reorientation.

## Slide 12
Progress to Date - Phase 0 Complete & Validated
12
Milestone | Status | Evidence
Isaac Lab 2.3.0 + Isaac Sim 5.1.0 installed | DONE | Python 3.11, torch 2.7.0+cu128
Headless GPU compatibility retired as a risk | DONE | PPO run, exit 0, checkpoint saved
Shadow Hand task validated | DONE | 20 epochs @ 8192 envs, 87 s
Gemini integration (replacing OpenAI) | DONE | Provider layer + model resolver
Both hand tasks registered in Eureka | DONE | Shadow + LEAP in TASKS_CFG
FULL EUREKA LOOP END-TO-END | DONE | 2 cand. x 2 iters, exit 0, 761 s
Concurrency ceiling measured | DONE | 2 workers max (3 exhausts RAM)
TWO SILENT-FAILURE BUGS FOUND & FIXED
-------------------------------------
1. Gemini rejects n>1 with HTTP 400
"Multiple candidates is not enabled"
-> would CRASH on the first LLM call
-> fix: detect + fan out to N calls,
result cached per process
2. Kit structured-log race with parallel
workers: RingBuffer corruption killed
one worker SILENTLY
-> 0 errors single-process, 4 with 2
-> fix: stagger worker startup
Both would have degraded the search
without raising any error.
• Gemini-authored reward code already includes quaternion double-cover handling, temperature-scaled shaping, and multiplicative task reward.

## Slide 13
Evaluation Plan - Staged Ablation Ladder
13
Rung | Configuration | Isolates | Primary metric
1 | Eureka/DrEureka reproduction, static DR | Baseline control | Task fitness F
2 | + Adaptive DR | Adaptive DR alone | Transfer to held-out config
3 | + PINN diagnosis & routing | Physics diagnosis, marginal | AUC + placebo delta
4 (optional) | + Learned failure summarizer | Learned vs hand-crafted reflection | 2x2 placebo
• One component changes per rung. Everything not under test - prompting, population size, PPO hyperparameters, fitness - is held identical.
• Transfer evidence differs by platform and must not be conflated:
• LEAP Hand - zero-shot on the PHYSICAL robot (DrEureka protocol).
• Shadow Hand - held-out perturbed sim config, never seen in training or DR. This is sim-to-OOD-sim, and will be labelled as such.
• No results are claimed yet. Review 1 reports the validated pipeline and the measured cost model; rung numbers follow.

## Slide 14
Risk Analysis & Mitigation
14
Risk | Prob. | Impact | Mitigation / current status
Contact discontinuity defeats the physics residual | High | High | Contact-phase gating; injection AUC gate runs BEFORE the router is built, so it fails cheaply
Candidate pool capped at 2 vs Eureka's 16 | Certain | High | MEASURED limit. Options: fewer candidates + more iterations, fewer envs/worker, sequential, or larger GPU. Stated as a deviation, not hidden
lam weights have no literature default | Certain | Med | Explicit tunable config; both source papers leave them untuned
Compounding adaptivity overfits a moving target | Med | Med | Freeze DR + PINN state before final transfer eval
Single task per platform (Isaac Lab has ~4-5 hand tasks) | Certain | Med | Stated as a limitation; breadth is future work

## Slide 15
Evaluation Rubric - CO Mapping
15
No. | Parameter | Marks | CO1 | CO2 | CO3 | CO4
1 | Project title & technical relevance | 1 | - | Y | - | Y
2 | Abstract & problem definition | 1 | - | Y | - | Y
3 | Objectives & expected outcome | 1 | - | Y | - | Y
4 | Scope & feasibility | 1 | Y | - | - | Y
5 | Preliminary work plan | 1 | Y | - | Y | Y

## Slide 16
Key References
16
• Y. J. Ma et al., "Eureka: Human-Level Reward Design via Coding Large Language Models," ICLR 2024.
• Y. J. Ma et al., "DrEureka: Language Model Guided Sim-To-Real Transfer," RSS 2024.
• J. Schulman et al., "Proximal Policy Optimization Algorithms," arXiv:1707.06347, 2017.
• M. Raissi, P. Perdikaris, G. E. Karniadakis, "Physics-Informed Neural Networks," J. Comput. Phys., vol. 378, 2019.
• I. Akkaya et al., "Solving Rubik's Cube with a Robot Hand," arXiv:1910.07113, 2019. (Automatic Domain Randomization)
• W. Li et al., "PIN-WM: Physics-Informed World Models for Non-Prehensile Manipulation," 2025.
• R. Fareh et al., "Physics-informed reward shaped RL control of a robot manipulator," Ain Shams Eng. J., 2025.
• K. Shaw, A. Agarwal, D. Pathak, "LEAP Hand: Low-Cost, Efficient, Anthropomorphic Hand for Robot Learning," RSS 2023.
• NVIDIA, Isaac Lab 2.3.0 / Isaac Sim 5.1.0 documentation, 2026.
• Y. Chen et al., "Bi-DexHands: Bimanual Dexterous Manipulation with RL," IEEE TPAMI, 2023.

## Slide 17
Thank You - Questions?
github.com/eureka-research/Eureka
github.com/eureka-research/DrEureka
github.com/NVlabs/IsaacLabEureka
github.com/isaac-sim/IsaacLab
github.com/leap-hand/LEAP_Hand_Isaac_Lab