## Slide 1
Physics-Informed Adaptive Domain Randomization
Stage 2: 2-DOF Testbed + LEAP Hand — Environment Build, RAPP, Physics-Informed Observer
Final Year Project | Review 2 | Team: [Name / Roll], [Name], [Name] | Guide: [Name] | 16 Sep 2026
All numbers in this deck are measured on this machine (NVIDIA L4, Isaac Lab 2.3.0) — none are carried over from the Stage-1 document without re-derivation.

## Slide 2
Recap — Stage 1: Eureka vs Human Reward (as documented)
2
• Benchmark documented in Stage-1 report:
• 2-DOF planar torque-controlled arm, Isaac Lab, PPO, 4096 parallel envs
• Human reward: R = -d + 5*I(d<0.05) - 0.005||a||^2
• Eureka reward: R = exp(-10d) + 100*I(d<0.05) - 0.01||qdot||^2 - 0.1
• Documented headline claim:
• Eureka: fast coarse reaching, weak fine precision (2 cm / 1 cm)
• Human reward: claimed to reach 98.4% @2cm, 79.7% @1cm after 5000 iters
• Central interpretation offered:
• "Eureka changes the objective; PPO changes the policy" — the +100 success bonus dwarfs the residual shaping once inside 5 cm
• Status found at the start of THIS stage:
- No corresponding code, checkpoints, or logs existed anywhere on this machine for those numbers.
STAGE-1 DOCUMENTED RESULTS
(reproduced here for reference only)
5cm 2cm 1cm med.err
Human PPO 99.49% 98.36% 79.74% 6.3mm
Eureka@500 97.90% 19.02% 3.56% 34.6mm
Eureka@1500 95.30% 18.10% 5.30% 33.3mm
-> This stage's job: BUILD the benchmark
for real, verify it, and see what
actually reproduces.

## Slide 3
Stage 2 Scope — Two Parallel Tracks
3
Track | Platform | Task | Why
A | 2-DOF planar arm (built from scratch) | reach a random goal marker | cheap, fast testbed for RAPP -> PINN -> adaptive DR
B | LEAP Hand (16-DOF) | Isaac-Reorient-Cube-Leap (upstream, unmodified) | real platform, published config, direct comparability
• Roadmap followed for Track A (physics-informed adaptive DR document):
• Freeze baseline -> static per-env DR -> RAPP -> PINN + uncertainty -> (adaptive DR: explicitly deferred)
• Roadmap's own checklist item 9: "Do not build the adaptive controller yet"
• Respected literally — items 1-12 done, items 13+ (adaptive DR, A-G ablation matrix) intentionally not started
• Track B: stock upstream task + hyperparameters, no modification
• So results stay comparable to the published LEAP Hand benchmark

## Slide 4
What Was Built (Track A) — No 2-DOF Code Existed Before This
4
• Environment
• Isaac Lab DirectRLEnv: URDF -> USD, torque control, 8-D obs, 2-D action
• 120 Hz physics / 30 Hz control, 10s episodes, 4096 parallel envs
• Domain randomization
• Per-env xi = [m1,m2,f1,f2,b1,b2,a1,a2] — friction, damping, mass, actuator effectiveness
• Sampled once per episode per env; read back from simulator to verify (not assumed)
• RAPP (Reward-Aware Physics Prior, DrEureka-style)
• One-parameter-at-a-time feasibility sweep -> measured C_RAPP envelope
• Physics-informed observer (PINN)
• Closed-form 2-link dynamics + 5-member deep ensemble -> infers xi from (q,qdot,tau,qddot)
• Evaluation harness
• One frozen metric definition (precision curve, settling time, effort) used everywhere
pi_adr/
source/pi_adr/
tasks/two_dof_reach/ env + cfg + PPO yaml
assets/ URDF, cached USD
pinn/ dynamics.py, model.py
evaluation/ metrics.py, runner.py
scripts/
validate_env.py 10/10 physics checks
validate_dynamics.py closed-form vs PhysX
pd_baseline.py IK+PD precision ceiling
run_rapp.py feasibility sweep
collect_pinn_data.py dynamics dataset
train_pinn.py observer + uncertainty
eval.py / eval_leap.py frozen metric suite
results/ EXPERIMENT_LOG.md RESULTS_2026-09-16.md

## Slide 5
Environment Validated Before Any Result Was Trusted
5
# | Check | Result
A | 30 Hz control / 120 Hz physics / 300 steps per episode | PASS
B | Simulated end-effector position == analytic forward kinematics | PASS (0.000 mm error)
C | Zero torque -> no drift (planar arm, g(q)=0) | PASS
D | a=+1 -> ~20 Nm on joint 1, positive rotation | PASS
E | Joint velocity respects +/-5 rad/s under saturated torque | PASS
F | Targets sampled r~U(0.20,0.85), inside 1.0 m reach | PASS
G | 8-D observation layout matches spec exactly | PASS
H | Vanilla & Eureka reward code == report equations 7/8 | PASS (0.00 deviation)
I | Domain randomization reaches the simulator, differs per env | PASS
J | Actuator effectiveness enters the coupled dynamics correctly | PASS (3.99% dev.)
10 / 10 CHECKS PASSED
DYNAMICS CROSS-CHECK
(closed-form 2-link model vs PhysX)
Forward dynamics (qdd):
mean relative error 2.27%
Inverse dynamics (recovered torque):
mean abs error 0.036 Nm
(torques up to 20 Nm)
-> physics residual used by the PINN
is measuring something real.
• Both validators re-run after every environment change — this discipline is what caught 3 of the 5 defects on the next slide.

## Slide 6
Five Defects Found and Fixed — Each Would Have Invalidated Results
6
# | Defect | Effect measured | Status
1 | Terminal error recorded AFTER env auto-reset | Trained policy scored 0.39% @5cm instead of 93% | Fixed
2 | ImplicitActuatorCfg damping=0 silently overrode URDF's 0.05 | Nominal physics != DR at scale 1.0 | Fixed
3 | Hard +/-pi joint limits create a wrap-around trap | Caps ANY controller at ~69% @5cm | Fixed
4 | PINN accel. labels differenced over a control step, not a physics step | True-xi RMSE 78.8 rad/s^2 (worse than the model!) | Fixed
5 | Mass randomization skipped the write at scale=1.0 | RAPP mass sweep: nominal scored 0.816 instead of 0.975 | Fixed
• Defect 3 is the important one for interpreting Stage 1:
• A scripted IK+PD controller under +/-pi limits fails 31.4% of episodes, and 100% of those failures end stalled against a joint stop -> the Stage-1 report's 99.49% is unreachable by ANY controller under such limits, so its joints were not actually bounded that way.

## Slide 7
Key Finding — The Environment Permits 1 mm Precision
7
• Question: is the ~30 mm error floor a property of the robot, or of the reward?
• Method: scripted 2-link inverse kinematics + PD control
• q* = IK(target), tau = Kp(q*-q) - Kd*qdot, through the SAME 20 Nm action interface as the learned policy
• Measured with the identical frozen metric suite — not a separate protocol
Controller | <5cm | <1cm | <1mm | median err
IK + PD (scripted) | 100% | 100% | 100% | 0.0 mm
Vanilla PPO @5000 | 93.0% | 2.2% | 0.02% | 34.7 mm
Eureka PPO @1500 | 99.1% | 7.9% | 0.05% | 30.1 mm
CONCLUSION
An optimal controller reaches 100%
success at EVERY threshold down to
1 mm on this exact benchmark.
-> The ~30mm floor of the learned
policies is a REWARD / LEARNING
result, not a robot/control-rate
limitation.
This is what makes the reward
comparison on the next slide
scientifically meaningful.

## Slide 8
Headline Results — Reproduced on the Corrected Benchmark
8
Metric | Stage-1 report (Eureka@500) | Ours (Eureka@500) | Stage-1 report (Eureka@1500) | Ours (Eureka@1500)
<5 cm | 97.90% | 96.97% | 95.3% | 99.05%
<2 cm | 19.02% | 25.56% | 18.1% | 26.37%
<1 cm | 3.56% | 3.59% | 5.3% | 7.91%
mean err | 33.5 mm | 46.4 mm | 45.5 mm | 38.6 mm
• The Eureka rows reproduce closely — coarse-success / fine-precision collapse confirmed.
• The vanilla (human-reward) row does NOT reproduce:
Metric | Stage-1 report (vanilla) | Ours (vanilla @5000)
<2 cm | 98.36% | 13.28%
<1 cm | 79.74% | 2.22%
TWO MEASURED CAUSES (not speculation)
1. Precision incentive is weak:
3cm->0.5cm gain ~0.6% of episode
return under the vanilla reward
2. Action sigma collapses:
1.0 -> ~0.024 during training
(report states 0.10-0.11 late-train)
-> exploration dies before fine
refinement is found
RESULT: on THIS build, Eureka beats
vanilla at every threshold.

## Slide 9
Domain-Randomization Robustness — A Secondary Finding
9
Policy | Physics | <5cm | <2cm | <1cm | mean err | mean qdot
Eureka@1500 | nominal | 99.05% | 26.37% | 7.91% | 38.6 mm | 2.52 rad/s
Eureka@1500 | in-distribution DR | 97.88% | 34.89% | 9.30% | 45.9 mm | 1.28 rad/s
Eureka@1500 | shifted (unseen) DR | 91.14% | 42.36% | 11.47% | 107.0 mm | 0.95 rad/s
• Harder physics DEGRADES coarse success (99% -> 91% @5cm) but IMPROVES fine precision (26% -> 42% @2cm).
• Mechanism: friction/damping/weaker actuators force the slowness the reward never explicitly asked for — mean joint velocity falls 2.52 -> 0.95 rad/s.
• This independently supports the Stage-1 thesis: the precision gap is an objective-design problem, not a capability problem — a slower policy (forced by physics, not reward) is a more precise one.
• Caution for future DR work: some apparent "robustness gain" under DR may just be physics doing the regularization the reward omits.

## Slide 10
RAPP — Reward-Aware Physics Prior (DrEureka protocol)
10
• One-parameter-at-a-time feasibility sweep on the nominal Eureka policy
• S(pi,xi) = P(d<5cm | pi,xi), feasible when S >= alpha = 0.9
• Measured C_RAPP envelope (all others held nominal while sweeping one):
Parameter | Feasible range | Note
friction | [0.0, 4.0] N.m | fails above 4 (S drops to 0.84 at 8)
damping scale | [0.25, 256] x nominal | very wide — nearly flat performance
actuator effectiveness | [0.3, 1.0] | fails below 0.3 — weak motors cannot compensate
mass scale | [1.0, 4.0] x nominal | ASYMMETRIC: fails with LIGHTER links, tolerates heavier
WHY MASS IS ASYMMETRIC
Lighter links -> more acceleration
per unit torque -> a policy tuned to
nominal inertia OVERSHOOTS.
Direct link to the precision finding
on the previous slide: the same
mechanism (torque/inertia mismatch)
explains both results.
IMPORTANT for future adaptive DR:
envelope is very wide & mostly FLAT
for 3 of 4 parameters -> may already
cover the region where adaptive DR
has little left to exploit.

## Slide 11
Physics-Informed Observer (PINN) — Architecture
11
CLOSED-FORM 2-LINK DYNAMICS (verified vs PhysX)
M(q;xi) qdd + C(q,qdot;xi) + F(qdot;xi) = alpha (.) tau_cmd
g(q) = 0 (planar, proven not assumed)
alpha on the RHS (keeps actuator effectiveness
identifiable from commanded torque)
xi = [m1,m2, f1,f2, b1,b2, a1,a2] in R^8
OBSERVER
input : window of 64 transitions (q,qdot,tau,qddot)
model : set-encoder (per-transition MLP + mean/max pool)
-- NOT a sequence model: EOM is instantaneous
output: xi_hat (bounded, hard constraint) + log(var)
ensemble: 5 independently-initialized members
-> U_PINN = epistemic + aleatoric variance
• Loss
• L = L_data (accel. MSE) + 0.01*L_phys (EOM residual) + L_sup (NLL vs ground-truth xi)
• Dataset discipline
• Interpolation / extrapolation splits use NON-OVERLAPPING physics ranges
• Velocity-saturated transitions masked out (limit engages ~4 rad/s, not 5)
• Critical fix made here
- Accel. labels were originally differenced over a 4-substep control step -> even the TRUE xi gave 78.8 rad/s^2 residual (worse than the trained model). Fixed by differencing over one physics step (1/120s) -> true-xi residual drops to 6.7 rad/s^2.

## Slide 12
PINN Results — Validated by Physics Configuration, Not Time Samples
12
 | accel. RMSE | param. error (norm) | uncertainty<->error rank corr.
Interpolation (held-out physics, same ranges) | 2.79 rad/s^2 | 0.065 | +0.11
Extrapolation (ranges outside training) | 12.28 rad/s^2 | 0.209 | +0.10
NEGATIVE RESULT — flagged, not hidden
• Ensemble uncertainty is only weakly related to its actual error (rank corr. ~+0.11, both splits).
• The roadmap's adaptive-DR score gives uncertainty (U_PINN) its own weighted term — on this evidence, that term would be close to noise.
• Before adaptive DR depends on it: either calibrate the uncertainty (current estimate uses only the DIAGONAL of the ensemble covariance — m and alpha are not independently identifiable from a single torque regime) or set its weight to zero.
• Extrapolation degrading 3x (0.065 -> 0.209) is the expected, honest result — supports keeping any future adaptive DR inside C_RAPP.

## Slide 13
Track B — LEAP Hand (Real Platform, Stock Configuration)
13
• Task: Isaac-Reorient-Cube-Leap (github.com/leap-hand/LEAP_Hand_Isaac_Lab)
• Config and hyperparameters UNMODIFIED (GRU-256, horizon 32, minibatch 32768, lr 5e-4 adaptive)
• Two upstream/Isaac-Lab-2.3 incompatibilities found & patched:
• train.py imported dump_pickle, removed from isaaclab.utils.io in 2.3 -> used our own wrapper train script
• EventCfg missing 'operation' arg now required by randomize_actuator_gains -> one-line fix (set 'abs' = the 2.1 default it was written against)
• Training: 500 PPO iterations, 4096 envs, seed 42
• Return: 33.09 (5-iter smoke test) -> 84,254.54 (500 iters)
RESULT (rung-1 reproduction baseline)
rotations / 20s / hand : 7.52
mean joint velocity : 1.86 rad/s
mean control effort : 0.70 / joint
(DrEureka's own reported metric for
this exact task — after only 500
iterations; DrEureka trains longer)
STATUS: baseline established.
No adaptive DR / PINN applied to
this track yet — Track A validates
the method first (cheaper iteration).

## Slide 14
Status Against the Roadmap's Immediate Checklist
14
# | Item | Status
1 | Freeze the 2-DOF environment and PPO baseline | DONE
2 | physics_params of shape [num_envs, N] | DONE (8-D xi per env)
3-4 | Friction randomization; verify all envs differ | DONE, read back from sim
5 | Fixed-policy sweep, terminal error vs friction | DONE (physics-performance map)
6 | Actuator effectiveness randomization | DONE
7-8 | Reproduce RAPP; store bounds | DONE (measured envelope)
9 | Do NOT build the adaptive controller yet | RESPECTED
10-11 | Standalone PINN; validate on unseen physics | DONE
12 | Add ensemble uncertainty | DONE (+ shown to be weak)
13+ | Adaptive DR outer loop, A-G ablation matrix | NOT STARTED (by design)
12 / 12 planned items complete

## Slide 15
A-G Matrix, n=5 seeds, Nominal Physics (mean ± std)
15
Rung | Setup | Mean err (mm) | Worst 10% (mm) | 5cm % | 2cm %
A | human, no DR | 37.8 ± 4.0 | 149 ± 32 | 98.5 | 29.0
B | Eureka, no DR | 37.7 ± 9.4 | 139 ± 74 | 99.0 | 26.9
C | human + static DR | 36.4 ± 7.2 | 136 ± 69 | 96.3 | 29.3
D | Eureka + RAPP static DR | 37.8 ± 8.1 | 147 ± 70 | 97.5 | 26.8
E | adaptive DR, no RAPP | 39.4 ± 5.5 | 109 ± 39 | 80.4 | 20.9
F4 | RAPP + adaptive DR | 44.7 ± 14.6 | 202 ± 145 | 94.1 | 23.1
G | F4 + PINN-scaled steps | 34.1 ± 3.9 | 82 ± 33 | 94.1 | 19.1
G placebo | shuffled multipliers (n=5) | 33.7 ± 4.0 | 87 ± 45 | 94.4 | 22.2
• Exact permutation tests: A/B/C indistinguishable (p>=0.18); F4 does not beat D; G vs F4 not significant (p 0.12-0.29)
• Placebo matches G on nominal and DRtrain (p>=0.74); the DRshift signal (p=0.024 at n=5) did not replicate at n=10 (p=0.281)
• Source: pi_adr/results/MATRIX_A_to_G.md

## Slide 16
Summary of Findings
16
• Confirmed
• Eureka's coarse-success / fine-precision collapse reproduces on an independently rebuilt benchmark; the environment itself permits 1mm (IK+PD 100%)
• Corrected after multi-seed testing
• Eureka does not beat the human reward at matched budget; vanilla's precision gap was largely PPO entropy collapse
• Single-seed wins for adaptive DR (F4, E) did not survive n=5; E loses nominal 5cm success (80% vs 97.5%, p=0.008)
• Static DR lowers 2cm success under DR evals vs no DR (21% vs 41%, p=0.016)
• PINN contribution: not demonstrated
• G has the lowest mean/tail error and spread, but is not significant vs F4 and the n=5 shuffled-multiplier placebo matches it on nominal/DRtrain (DRshift p=0.024 at n=5 did not replicate at n=10: p=0.281)
• Observer uncertainty is weakly informative and unreliable outside its training range (extrapolation rank corr -0.16)
• Process
• Five silent-failure defects found and fixed; overclaims retracted openly in the log

## Slide 17
Next Steps
17
• Immediate
• Retest done (n=10): no G benefit. Move to LEAP Hand (Track B)
• LEAP Hand: no-ADR baseline, native ADR, RAPP-initialised ADR (Track B)
• If pursuing the PINN idea
• Observer reliable outside its training envelope; uncertainty weighting that is not dominated by one dimension
• Longer training budgets than 800 iterations
• Longer-term
• Sim-to-real hardware stage after robust simulation policies are established